## Slide 1: Computer Networks IP ADDRESSING
Dr. Muhammad Nadeem Majeed
Contact info:
nadeem.majeed@pucit.edu.pk
0333-1049181
PUCIT, University of the Punjab, Lahore

## Slide 2
IP ADDRESSING

## Slide 3
IP Addressing
IP Addressing is Logical Addressing
It works on Network Layer (Layer 3)
Two Versions of Addressing Scheme
  IP version 4 – 32 bit addressing
  IP version 6 – 128 bit addressing

## Slide 4
Bit is a value that will represent 0’s or 1’s (i.e. Binary)
01010101000001011011111100000001
32 bits are divided into 4 Octets known as Dotted Decimal Notation
01010101. 00000101. 10111111. 00000001
IP version 4
First Octet Second Octet Third Octet Forth Octet

## Slide 5
128-bit address is divided along 16-bit boundaries, and each 16-bit block is converted to a 4-digit hexadecimal number and separated by colons (Colon-Hex Notation) FEDC:BA98:7654:3210:FEDC:BA98:7654:3210
IP version 6

## Slide 6
Taking Example for First Octet :
Total 8 bits, Value will be 0’s and 1’s
i.e. 28 = 256 combination
27 26 25 24 23 22 21 20
0 0 0 0 0 0 0 0 = 0
0 0 0 0 0 0 0 1 = 1
0 0 0 0 0 0 1 0 = 2
0 0 0 0 0 0 1 1 = 3
0 0 0 0 0 1 0 0 = 4
Binary to Decimal Conversion
1 1 1 1 1 1 1 1 = 255
Total IP Address Range
0 . 0 . 0 . 0
to
255.255.255.255

## Slide 7
Total IP Addressing Scheme is divided
into 5 Classes
CLASS A
CLASS B
CLASS C
CLASS D
CLASS E
IP Address Classes
LAN & WAN
Multicasting
Research & Development

## Slide 8
Priority Bit Concept
To identify the range of each class
a bit called priority bit is used.
Priority Bit is the left most bits in the First Octet
CLASS A priority bit is 0
CLASS B priority bit is 10
CLASS C priority bit is 110
CLASS D priority bit is 1110
CLASS E priority bit is 1111

## Slide 9
For Class A range : First bit of the first octet
should be reserved for the priority bit.
0xxxxxxx. xxxxxxxx. xxxxxxxx. xxxxxxxx
27 26 25 24 23 22 21 20
0 0 0 0 0 0 0 0 = 0
0 0 0 0 0 0 0 1 = 1
0 0 0 0 0 0 1 0 = 2
0 0 0 0 0 0 1 1 = 3
0 0 0 0 0 1 0 0 = 4
CLASS A Range
0 1 1 1 1 1 1 1 = 127
Class A Range
0 . 0 . 0 . 0 to
127.255.255.255
Exception
0.X.X.X and 127.X.X.X network are reserved

## Slide 10
For Class B range : First two bits of the first
octet should be reserved for the priority bit.
10xxxxxx. xxxxxxxx. xxxxxxxx. xxxxxxxx
27 26 25 24 23 22 21 20
1 0 0 0 0 0 0 0 = 128
1 0 0 0 0 0 0 1 = 129
1 0 0 0 0 0 1 0 = 130
1 0 0 0 0 0 1 1 = 131
1 0 0 0 0 1 0 0 = 132
CLASS B Range
1 0 1 1 1 1 1 1 = 191
Class B Range
128. 0 . 0 . 0
to
191.255.255.255

## Slide 11
For Class C range : First Three bits of the first
octet should be reserved for the priority bit.
110xxxxx. xxxxxxxx. xxxxxxxx. xxxxxxxx
27 26 25 24 23 22 21 20
1 1 0 0 0 0 0 0 = 192
1 1 0 0 0 0 0 1 = 193
1 1 0 0 0 0 1 0 = 194
1 1 0 0 0 0 1 1 = 195
1 1 0 0 0 1 0 0 = 196
CLASS C Range
1 1 0 1 1 1 1 1 = 223
Class C Range
192. 0 . 0 . 0
to
223.255.255.255

## Slide 12
For Class D range : First four bits of the first
octet should be reserved for the priority bit.
1110xxxx. xxxxxxxx. xxxxxxxx. xxxxxxxx
27 26 25 24 23 22 21 20
1 1 1 0 0 0 0 0 = 224
1 1 1 0 0 0 0 1 = 225
1 1 1 0 0 0 1 0 = 226
1 1 1 0 0 0 1 1 = 227
1 1 1 0 0 1 0 0 = 228
CLASS D Range
1 1 1 0 1 1 1 1 = 239
Class D Range
224. 0 . 0 . 0
to
239.255.255.255

## Slide 13
For Class E range : First four bits of the first
octet should be reserved for the priority bit.
1111xxxx. xxxxxxxx. xxxxxxxx. xxxxxxxx
27 26 25 24 23 22 21 20
1 1 1 1 0 0 0 0 = 240
1 1 1 1 0 0 0 1 = 241
1 1 1 1 0 0 1 0 = 242
1 1 1 1 0 0 1 1 = 243
1 1 1 1 0 1 0 0 = 244
CLASS E Range
1 1 1 1 1 1 1 1 = 255
Class E Range
240. 0 . 0 . 0
to
255.255.255.255

## Slide 14
IP address is divided into Network & Host Portion
CLASS A is written as N.H.H.H
CLASS B is written as N.N.H.H
CLASS C is written as N.N.N.H
Octet Format

## Slide 15
CLASS A – No. Networks & Host
Class A Octet Format is N.H.H.H
Network bits : 8 Host bits : 24
No. of Networks
= 28-1 (-1 is Priority Bit for Class A)
= 27
= 128 – 2 (-2 is for 0 & 127 Network)
= 126 Networks
No. of Host
= 224 – 2 (-2 is for Network ID & Broadcast ID)
= 16777216 - 2
= 16777214 Hosts/Network
CLASS A
126 Networks
&
16777214 Hosts/Nw

## Slide 16
CLASS B – No. Networks & Host
Class B Octet Format is N.N.H.H
Network bits : 16 Host bits : 16
No. of Networks
= 216-2 (-2 is Priority Bit for Class B)
= 214
= 16384 Networks
No. of Host
= 216 – 2 (-2 is for Network ID & Broadcast ID)
= 65536 - 2
= 65534 Hosts/Network
CLASS B
16384 Networks
&
65534 Hosts/Nw

## Slide 17
CLASS C – No. Networks & Host
Class C Octet Format is N.N.N.H
Network bits : 24 Host bits : 8
No. of Networks
= 224-3 (-3 is Priority Bit for Class C)
= 221
= 2097152 Networks
No. of Host
= 28 – 2 (-2 is for Network ID & Broadcast ID)
= 256 - 2
= 254 Hosts/Network
CLASS C
2097152 Networks
&
254 Hosts/Nw

## Slide 18
The network address is represented with all bits as ZERO in the host portion of the address
The broadcast address is represented with all bits as ONES in the host portion of the address
Valid IP Addresses lie between the Network Address and the Broadcast Address.
Only Valid IP Addresses are assigned to hosts/clients
Network & Broadcast Address

## Slide 19
Class A : N.H.H.H
Network Address :
0xxxxxxx.00000000.00000000.00000000
Broadcast Address :
0xxxxxxx.11111111.11111111.11111111
Example - Class A
Class A
10.0.0.0
10.0.0.1
10.0.0.2
10.0.0.3
10.255.255.254
10.255.255.255
Broadcast Address
Network Address
Valid IP Addresses

## Slide 20
Class B : N.N.H.H
Network Address :
10xxxxxx.xxxxxxxx.00000000.00000000
Broadcast Address :
10xxxxxx.xxxxxxxx.11111111.11111111
Example - Class B
Class B
172.16.0.0
172.16.0.1
172.16.0.2
172.16.0.3
172.16.255.254
172.16.255.255
Broadcast Address
Network Address
Valid IP Addresses

## Slide 21
Class C : N.N.N.H
Network Address :
110xxxxx.xxxxxxxx.xxxxxxxx.00000000
Broadcast Address :
110xxxxx.xxxxxxxx.xxxxxxxx.11111111
Example - Class C
Class C
192.168.1.0
192.168.1.1
192.168.1.2
192.168.1.3
192.168.1.254
192.168.1.255
Broadcast Address
Network Address
Valid IP Addresses

## Slide 22
There are certain addresses in each class of IP address that are reserved for LAN. These addresses are called private addresses.
They can be used for: home & office networks, networks not connected to Internet.
Private IP Address
Class A
10.0.0.0 to 10.255.255.255
Class B
172.16.0.0 to 172.31.255.255
Class C
192.168.0.0 to 192.168.255.255

## Slide 23
Subnet Mask
Subnet Mask differentiates Network portion and Host Portion
Subnet Mask is been given for host Identification of Network ID
Represented with all 1’s in the network portion
and with all 0’s in the host portion.

## Slide 24
Class A : N.H.H.H
11111111.00000000.00000000.00000000
Default Subnet Mask for Class A is 255.0.0.0
Class B : N.N.H.H
11111111.11111111.00000000.00000000
Default Subnet Mask for Class B is 255.255.0.0
Class C : N.N.N.H
11111111.11111111.11111111.00000000
Default Subnet Mask for Class C is 255.255.255.0
Subnet Mask - Examples

## Slide 25
How Subnet Mask Works ?
IP Address : 192.168.1.1
Subnet Mask : 255.255.255.0
ANDING PROCESS :
192.168.1.1 = 11000000.10101000.00000001.00000001
255.255.255.0 = 11111111.11111111.11111111.00000000
=======================================
192.168.1.0 = 11000000.10101000.00000001.00000000
=======================================
The output of an AND table is 1 if both its inputs are 1.
For all other possible inputs the output is 0.
AND TABLE
A B C
0 0 0
0 1 0
1 0 0
1 1 1

## Slide 26
Dividing a Single Network into Multiple Networks.
Converting Host bits to Network Bits
i.e. Converting 0’s into 1’s
Subnetting is also called as FLSM (Fixed Length Subnet Mask)
Subnetting can be done in three ways.
  Requirement of Networks
  Requirement of Hosts
  Cisco / Notation
Subnetting

## Slide 27
ZOOM Technologies is having 100 PC
Which Class is preffered for the network ?
Answer : Class C.
In ZOOM Technologies we have Five Departments with 20 Pcs each
ZOOM Technologies – 192.168.1.0/24
Scenario
MCSE
192.168.1.1 to 192.168.1.20
192.168.1.21 to 192.168.1.40
CISCO
FIREWALL
192.168.1.41 to 192.168.1.60
SOLARIS
192.168.1.61 to 192.168.1.80
TRAINING
192.168.1.81 to 192.168.1.100

## Slide 28
Administrator’s Requirement :
Inter-department communication should not be possible ?
Solution.
Allocate a different Network to each Department
i.e.
Scenario (…continued)
MCSE
192.168.1.1 to 192.168.1.20
192.168.2.1 to 192.168.2.20
CISCO
FIREWALL
192.168.3.1 to 192.168.3.20
SOLARIS
192.168.4.1 to 192.168.4.20
TRAINING
192.168.5.1 to 192.168.5.20
In the above Scenario inter-department communication is not possible.

## Slide 29
Problem with the previous Scenario is :-
Loss of bandwidth as the broadcasting is done for 254 machines rather than for 20 machines.
Wastage of IP addresses (Approximately 1000)
No Security
Main Aim of Subnetting

## Slide 30
POWER TABLE
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
216 = 65536
217 = 131072
218 = 262144
219 = 524288
220 = 1048576
221 = 2097152
222 = 4194304
223 = 8388608
224 = 16777216
225 = 33554432
226 = 67108864
227 = 134217728
228 = 268435456
229 = 536870912
230 = 1073741824
231 = 2147483648
232 = 4294967296
Power table

## Slide 31
Some Important Values
VALUES IN SUBNET MASK
Bit Value Mask
1 128 10000000
2 192 11000000
3 224 11100000
4 240 11110000
5 248 11111000
6 252 11111100
7 254 11111110
8 255 11111111

## Slide 32
Requirement of Networks is 5 ?
Example – 1
No. of Host
= 2h – 2 (-2 is for Network ID & Broadcast ID)
= 25 – 2
= 32 – 2
= 30 Hosts/Subnet
Class C : N.N.N.H
110xxxxx.xxxxxxxx.xxxxxxxx.xxxxxxxx
Class C : 192.168.1.0
No. of Subnet
= 2n  Req. of Subnet
= 23  5
= 8 Subnet
110xxxxx.xxxxxxxx.xxxxxxxx.xxxxxxxx
HELP

## Slide 33
x
Example – 1 (Continued…)
Range of Networks
Network ID Broadcast ID
192.168.1.0
Customize Subnet Mask =
255.
11111111.
255.
11111111.
255.
11111111.
11100000
128
64
32
32
192.168.1.32
192.168.1.64
192.168.1.96
192.168.1.128
192.168.1.160
192.168.1.192
192.168.1.224
192.168.1.31
192.168.1.63
192.168.1.95
192.168.1.127
192.168.1.159
192.168.1.191
192.168.1.223
192.168.1.255
x
Valid Subnets
224
If you convert 3 Host Bits to Network Bits
8 Subnet & 30 Hosts/Subnet
Customize Subnet Mask
255.255.255.224
Subnet Range
192.168.1.32 to 192.168.1.63  MCSE .
192.168.1.64 to 192.168.1.95  CISCO .
192.168.1.96 to 192.168.1.127  FIREWALL
192.168.1.128 to 192.168.1.159  SOLARIS
192.168.1.160 to 192.168.1.191  TRAINING
192.168.1.192 to 192.168.1.223  Future Use

## Slide 34
Requirement of Networks is 14 ?
Example – 2
No. of Host
= 2h – 2 (-2 is for Network ID & Broadcast ID)
= 24 – 2
= 16 - 2
= 14 Hosts/Subnet
Class C : N.N.N.H
110xxxxx.xxxxxxxx.xxxxxxxx.xxxxxxxx
Class C : 192.168.1.0
No. of Subnet
= 2n  Req. of Subnet
= 24  14
= 16
= 16 Subnet
110xxxxx.xxxxxxxx.xxxxxxxx.xxxxxxxx
HELP

## Slide 35
x
Example – 2 (Continued…)
Range of Networks
Network ID Broadcast ID
192.168.1.0
Customize Subnet Mask =
255.
11111111.
255.
11111111.
255.
11111111.
11110000
128
64
32
x
Valid Subnets
16
16
192.168.1.224 – 192.168.1.239
192.168.1.240 – 192.168.1.255
– 192.168.1.15
192.168.1.16 – 192.168.1.31
192.168.1.32 – 192.168.1.47
192.168.1.48 – 192.168.1.63
240
If you convert 4 Host Bits to Network Bits
14 Subnet & 14 Hosts/Subnet
Customize Subnet Mask
255.255.255.240
Subnet Range
192.168.1.16 to 192.168.1.31
192.168.1.32 to 192.168.1.47
192.168.1.48 to 192.168.1.63
192.168.1.64 to 192.168.1.80
192.168.1.224 to 192.168.1.239

## Slide 36
THE END